City of Westbrook

DEPARTMENT OF COMMUNITY SERVICES

Maria Dibiase Dorn							                     Greg Post

Director                                                                                                                                             Deputy Director

____________________________________________________________________________

426 Bridge St                Westbrook, Maine 04092	          (207) 854-0676 Phone	     (207) 854-0628 Fax

# CITY OF WESTBROOK, MAINE

# COMMUNITY SERVICES DEPARTMENT

Sealed bids will be received in the Office of the City Clerk, 2 York Street, Westbrook, Maine 04092 until SEPTEMBER  12TH, 2013 AT 2:00 PM when they will be publicly opened and read for one:

1 TON 4x4 DUAL REAR WHEEL CAB / CHASSIS WITH STAINLESS STEEL  DUMP BODY, SANDER and SNOWPLOW.

Additional copies of the bid package may be obtained at the City Clerk’s office, (207) 854-9105.

# Jerre Bryant

City Administrator

# PAGE 1: BID FORM

#### COMMUNITY SERVICES DEPARTMENT BID FORM

#### ONE TON 4X4 DUMP TRUCK AND EQUIPMENT

We the undersign agree to furnish The City of Westbrook with the equipment

described in the preceding specifications, which are incorporated as part of this proposal at the following price and delivery date. This form maybe copied to allow for multiple vehicle proposals.

MANUFACTURER: ____________	  MODEL: __________   YEAR: _____

ENGINE SIZE: ________________         COLOR: __________

DELIVERY DATE: ____________

# PRICE: (WITH 6.2L AND 4.30LS AXLE) ___________________

WARRANTY: __________________________________

# DEALERSHIP: ________________________________________________

ADDRESS: __________________________________________________

CITY / TOWN: _____________________________	STATE: __________

TELEPHONE: ________________________	FAX: __________________

AUTHORIZED SIGNATURE: _____________________________

# TITLE: ______________________________________

# PAGE 1: INSTRUCTIONS & CONDITIONS

# CITY OF WESTBROOK, MAINE

INSTRUCTIONS AND GENERAL CONDITIONS TO BIDDERS

1.	SUBMISSIONS OF BIDS:

#### Bids shall be submitted on the BID FORM provided in this package  and must be marked clearly on the outside:

1 TON 4x4 DUMP TRUCK

#### The envelope shall be addressed to: City of Westbrook, ATTN: Lynda Adams, 2 York Street, Westbrook, Maine 04092.

Any questions concerning the bid should be addressed to Shawn Adams (207) 831-7912 during the hours of 7:00 A.M. - 5:00 P.M.

The City of Westbrook reserves the right to reject any and all bids in whole or in part when deemed to be in the best interest of the City. The City may waive any minor discrepancy in the bid specification and will inspect the vehicle at the bidder's establishment prior to purchase.

# WARRANTIES, BROCHURE, MANUALS:

# All warranties and a descriptive brochure describing the equipment shall be enclosed in the bid. The bidder shall state the warranty period on the bid form. All appropriate parts and service manuals shall be delivered with the selected equipment.

# 3.	DISCOUNTS:

The City of Westbrook, pays its accounts in full within a thirty (30) day period following satisfactory completion of the contract and receipt of bills for all items covered by the City's purchase order. In submitting bids under these specifications, bidders should take into account all discounts allowed in accordance with the above payment policy.

# 4.	EXEMPTION FROM TAXES:

# The City is exempt from payment of federal excise taxes on articles not for resale, federal transportation tax on all shipments, and Maine State sales tax and use tax.

PAGE 2: INSTRUCTIONS & CONDITIONS

# 5.	TRANSPORTATION CHARGES:

All transportation and delivery charges including expenses for freight, transfer, mail, etc, shall be prepaid and be at the expense of the BIDDER unless otherwise specified in the bid.  The bid price shall include all installation charges.

# 6.	EXCEPTIONS or ADDITIONAL FEATURES:

Any exceptions to these bid requirements and specifications shall be clearly indicated by the bidder on a separate sheet of paper. In the absence of clearly noted exceptions, bidders will be obligated to comply with all the provisions contained herein. Any equivalent features and any additional features to those described in the specifications shall be so noted in the bid.

# 7.	DAMAGE REPAIR:

The BIDDER shall be held responsible for repairing, at their sole cost and expense, any and all damages to City or private property resulting from the work to be performed.

# 8.	SAFETY REGULATIONS:

The BIDDER will at times, comply with the safety regulations set forth by the Occupational Safety and Health Administration.

# 9.	DEFAULT:

In case of default by the bidder, the City of Westbrook reserves the right to procure the contract services from other sources and charge any excess cost occasioned by thereby to the BIDDER.

# 10.	ADDENDUM:

Should a BIDDER find discrepancies in or omissions from the specifications or other contract documents, or should a BIDDER be in doubt as to their meaning, the BIDDER shall at once contact or notify Shawn Adams at (207) 831-7912.

# 11.	BID OPENING:

All bids will be opened publicly and BIDDERS or their representatives may be present at the bid opening. The bids will be available for public inspection after opening but the City will not prepare abstracts for distribution.

PAGE 3: INSTRUCTIONS & CONDITIONS

# 12.	TERM OF BID:

The bid shall meet all the listed specifications. No BIDDER may withdraw a bid for a period of sixty (60) days after the actual date of opening.

# 13.	AWARD OF CONTRACT:

Award will be made to the lowest responsible BIDDER, taking into consideration the quality of the product or services; conformance with the specifications and intended purpose; delivery time; ultimate cost to the City and with the overall recommendation from the Director of Public Services. Sale is subject to City Council authorization by two affirmative votes or readings at two meetings of the council.

#### 1 TON 4x4 DUAL REAR WHEEL CAB / CHASSIS

All items appearing in the bidder's regular published specifications are assumed to be included in the bidder's proposal. The following specifications shall be the minimum requirements and the equipment proposed shall comply with Maine and Federal laws. All specifications, dimensions and ratings must conform to or exceed S.A.E. specifications where applicable.

INTENT:

The intent of the City of Westbrook is to purchase a one ton cab and chassis. It is not the intent of these specifications to favor any one manufacturer and, therefore, should not be considered restrictive.  It is intended, however, to derive acceptable performance criteria.   The City of Westbrook will entertain all bids submitted by Vendors that meets or is equivalent to the specifications requested (that could include a vehicle in current inventory) upon final review by the Director of Public Services.

INSTRUCTION TO BIDDERS:

The truck to be furnished under this bid shall be a one ton cab and chassis and include the following: dump body, snowplow, sander and hitch plate. It shall be the manufacturer’s latest model and design. These specifications shall be regarded as MINIMUM. Bidders must furnish all descriptive literature,

manufacturer’s compliance certificates and all other necessary data on the               equipment proposed as required in the specification. Bidder must answer

YES or NO to each specification line item except where asked to state specific data. Failure to answer correctly, or failure to respond, will deem your bid as non-responsive. All line items with a “NO” response, shall be explained in detail on the “Exceptions to Bid Specification” page provided at the end of this document.

PAGE 1: CHASSIS SPECIFICATIONS

1 TON 4x4 REGULAR CAB, DUMP TRUCK SPECIFICATIONS

All items appearing in the bidder's regular published specifications are assumed to be included in the bidder's proposal.  The following specifications shall be the minimum requirements and the equipment proposed shall comply with Maine and Federal laws. All specifications, dimensions and ratings must conform to or exceed S.A.E. specifications where applicable.

BODY STYLE and General Options

1 Ton 4X4 Cab and Chassis:					       _______

F-350 (Regular cab) or Equivalent, XL series 4X4; wheel base of 141”; 60” cab to axle length; minimum GVWR of 14,000 lbs. The vehicle shall include all the standard equipment plus the following accessories: Power/heated mirrors; power door locks; power windows; power steering; daytime running lights; AM/FM stereo with single CD changer radio; Sync with steering wheel controls; air conditioning; front premium cloth 40/20/40 seats;

6” black angular running boards. Exterior color is to be Oxford White with Steel Gray premium cloth interior.

If dealer has a vehicle with an accessory package exceeding these options it would be considered.

ENGINE:                                                                                           _______

6.2 liter, 2-Valve SOHC Electronic Fuel Injected

gasoline engine with 316 Horsepower; 397 FT.LB.

torque. CNG/LPG Gaseous engine prep package.

TRANSMISSION:	                                                                    _______

##### TorqShift Heavyduty, SelectShift

##### 6-speed automatic.

BRAKES:	                                                                                       _______

4-Wheel disc/4-Wheel Anti-lock braking

System; Engine only traction control;

Hydro-boost.

PAGE 2: CHASSIS SPECIFICATIONS

PAYLOAD PACKAGE:                                                                    _______

14,000 lbs. GVWR. Front axle rating of

6,000 lbs. and Rear axle rating of 9,750 lbs.

Axle ratio is to be 4:30 with limited slip.

TANSFER CASE:	                                                                     _______

Manual transfer case and hubs.

TIRES:	                                                                                       _______

LT245/75RX17, load range E. BSW All-

Terrain tires (6) mounted on steel wheels.

Spare tire and wheel (includes 4 ton hydraulic

jack).

COOLING SYSTEM:	                                                                     _______

Heavy duty for coolant, engine oil and

transmission fluids.

ELECTRICAL SYSTEM:                                                                  _______

157 amp alternator with a 650 CCA

battery. Chassis is to be equipped with

daytime running lights.

EXTERIOR:	                                                                     _______

Manually telescoping trailer tow mirrors

with  power/heated glass, integrated clearance

lights and turn signals (part of the power

equipment group). Front splash guards/flaps;

XL value package (96V): includes

chrome front bumper, dual beam jewel effect

headlights and under hood engine compartment

light. Cab steps, 6” black angular molded in

color running boards. Truck color - Oxford white.

Fuel tank capacity is to be 40 gallons.

PAGE 3: CHASSIS SPECIFICATIONS

INTERIOR:	                                                                     _______

Front bench seat – 40/20/40 with armrest, cup holder

and storage bin – Cloth. Interior, Steel in color.

Manual air conditioning. Power equipment group (90L)   Power locks and windows, upgraded mirrors.

###### ADDITIONAL PACKAGES:                                                             _______

The cab and chassis shall include the following

packages: Trailer Brake Controller (52B). This

will include integrated trailer brake controller and

trailer wiring – 7 wire harness w/relays, blunt cut

and labeled.

Upfitter switches are to be included. Factory installed     back up alarm. Snow Plow Prep Package (473).

PAGE 1: EQUIPMENT SPECIFICATIONS

W.A. Messer Co. (Attention Bob Tardiff), is the

preferred vendor for the installation of the

following equipment.

###### DUMP BODY:	                                                                     _______

Galion Model # 133UDS9, 2.3 to 3.5 yard capacity

dump body with low mount drop sides. GS515DA subframeless low mount double acting electric hydraulic hoist. All 10 gauge stainless steel  construction, 3/16” single piece floor and a double acting, quick release tailgate. Body will include a 24” cab protector and front and rear mounted mud flaps.

###### SNOW PLOW:	                                                                     _______

Fisher 9’  “XBlade”, Minute Mount II plow with

the following: 9’ stainless steel blade; 12 volt Insta-act hydraulics featuring the E-Force lighting and marker module, (1) piece reversible carbon steel cutting edge and fish-stik hand held control. The fish-stik control will have a button for each function.

###### INSERT SANDER:                                                                           _______

Fisher 2.0 yard (struck), 14 gauge stainless steel

sander with 11 H.P I/C Honda engine and electric

start. Sander to include the following: 12 volt

battery and box, electric clutch & throttle,

full cab controls, inverted “V”, extended

spinner (26”), heavy duty top screens, 16”

conveyor chain, and hold down kit.

###### HITCH PLATE:                                                                                 _______

Steel hitch plate, ½” steel plate, fully welded

construction, 2” receiver tube, pintle, ball (2”) combo hitch shall be included. Seven pin round style trailer plug (Public Services will supply a wiring diagram for the trailer plug) and a pair of D-rings.

PAGE 1: LIGHTING SPECIFICATIONS

###### LIGHTING:                                                                    		    _______

Whelen Mini Justice JY Series (1) Model  MJYAAAAP, Amber four linear6 corner modules and two JDC forward facing inner amber modules, permanent mount lightbar with a 40’ cable and (2) rear facing LR11 LED worklights. Lightbar is to be installed on the headboard on riser mounts.

(2) Whelen Vertex Amber LED hide-a-way’s, Model VTX609A, shall be installed in the marker light portion of the headlight assemblies. The headlight assemblies shall be completely sealed to prevent moisture and dirt from entering the headlight assemblies.

Whelen 500 series LED’s (2) Model 5VA02ZCR, 500 Series super LED lightheads with 5GROMMET mounts and 25’ cables. Cables and lightheads are to have Deutsch waterproof connectors installed on them. These are to be installed in the rear of the dump body in lieu of the extra brake/taillights.

(2) Soundoff auxiliary reverse/work lights, Model EWLC1400TBDTOW Trapezoid 5” Rectangle LED work lights are to be installed on the rear hitch plate as directed.

Activation of the warning lights will be done using the factory installed upfitter switch panel. The first switch will be for the Mini Edge lightbar. The second switch will be for the front hide-a-way LED’s. The third switch will be for the rear body mounted LED’s. The forth switch will used for the auxiliary reverse/work lights.

This switch will activate the (4) work lights, (2) in the lightbar and (2) on the hitch plate, only when in the on position. In the off position the (4) work lights will activate anytime the vehicle is in reverse. This shall be accomplished via a 30 amp relay.

The chassis reverse circuit will activate the relay which in turn will power up the work lights. The feed for the relay shall come from the auxiliary fuse panel.

PAGE 2: LIGHTING SPECIFICATIONS

There shall be an auxiliary six place ATC fuse panel with ground terminals installed behind the knee bolster under the steering column. This panel will be feed from the battery through an 80 amp, manual reset, waterproof circuit breaker.

The fuse panel with be ignition activated through a 75 amp Bosch relay. The fuse panel, 75 amp relay and 30 amp reverse relay shall all be mounted on aluminum plate.

All lighting wiring connections shall use crimp and heat shrink connectors, no exceptions. All wiring will be incased in split polyloom. All lighting shall be installed and work ready upon delivery. Any place where the wiring enters the cab shall include grommet protection and be sealed.

(1) Two way radio shall be supplied and installed. Radio shall be a Motorola PM 400 and include a unity gain antenna and antenna cable. The radio is to be mounted on the top of the dash in the “storage area” and to the left of the storage area. This shall be power via the auxiliary fuse panel. The antenna shall be mounted on the center, rear portion of the roof.

PAGE1: EXCEPTIONS

EXCEPTIONS TO BID SPECIFICATIONS

Feature			Explanation

__________			______________________________________

______________________________________

__________			______________________________________

______________________________________

__________			______________________________________

______________________________________

__________			______________________________________

______________________________________

__________			______________________________________

______________________________________

__________			______________________________________

______________________________________

__________			______________________________________

______________________________________

__________			______________________________________

______________________________________

__________			______________________________________

______________________________________