LETTERS OF INTEREST

AND STATEMENTS OF QUALIFICATIONS

For

Construction and Engineering Inspection Services

Circle Hill Road Project

Dear Vendor;

Thank you for your interest in doing business with the Jackson County Board of County Commissioners.  Currently, we are requesting Letters of Interest and Statements of Qualifications from registered, qualified consultant firms in the State of Florida with experience in Construction and Engineering Inspection Services on County Dirt Roads for projects involving Federal Emergency Managements and State of Florida reporting requirements, and inspection on projects involving restoring the roads to their condition prior to the storm event of April 2014:

Project:	Circle Hill Road Project

The Work involves paving the existing dirt road to 20 foot wide (two 10 foot lanes) and includes clearing and grubbing and trimming to existing maintained road width (existing width varies) or to 16 feet from center of existing dirt road, grading to typical section, dig out and remove unsuitable material (if encountered), grade shoulders (and ditches where the width allows) prior to placing limerock, 8" limerock base, the base will be primed with prime coat, 1-1/2" layer of SP 9.5 asphalt, finish grade the shoulders prior to placing sod, sod, seed and mulch, Maintenance of Traffic (MOT), paving driveways with 1-1/2" asphalt and 6" limerock, aprons, stormwater pollution prevention, grading ditches and/or shoulders to provide positive drainage, sod beside the road, driveways, and mitered ends, seed and mulch all other disturbed areas, and pipe replacement and mitered ends or headwalls as indicated in the plans, and striping and pavement markings.

This project involves Federal funding through FEMA and the State of Florida Emergency Management.

The consultant will provide on site inspectors to monitor the work of the contractor and to ensure that the roads are improved to the intent of the bid documents in support of the Jackson County Engineering and Road Departments. The roads involved are listed in the form of proposal along with the quantities of work.

The selected firm shall serve as the Jackson County Construction and Engineering Inspection Services consultant for the project.  Qualifications must be submitted by the deadline at the location as indicated below:

Due Date:	Wednesday, July 26, 2017 - 2:00 p.m. CST,

Jackson County Purchasing Department

2864 Madison Street, Marianna, Fl 32446

The consultant will be selected based on qualifications and experience for the type of Work and will strictly follow the Consultants Competitive Negotiations Act and the State of Florida rules and regulations.

Please direct any questions regarding these documents to Larry Alvarez at the Jackson County Engineering Department.  Questions must be submitted in writing by email to Larry Alvarez at lalvarez@jacksoncountyfl.com or faxed to (850) 482-9063, with a copy emailed to Jeannie Bean at jbean@jacksoncountyfl.com or faxed to Jeannie Bean at (850) 482-9063, and copy to Judy Austin at jaustin@jacksoncountyfl.com.  We look forward to working with you. A copy of the RFQ may also be found on our web page at www.jacksoncountyfl.net/commissioners and then click on Purchasing Department and then on bids/RFQ’s.