SECTION 00010

ADVERTISEMENT FOR BIDS

PROJECT NAME:     Bowden Hill Road

Sealed bids, submitted in triplicate, will be received by the Board of County Commissioners of Jackson County, Florida, (Owner), until     1:00 p.m. (Central Time)  August 31, 2017   at the County Engineer’s Office (County Engineer, Larry Alvarez), 2828 Owens Street, Marianna, FL 32446 for the construction of the following described Project:

Bowden Hill Road

The Work involves installing 40' of 30" RCP plus 2 headwalls, cutting and replacing the roads, excavation and backfill to install the pipe, 8" limerock base, prime coat, 1-1/2" layer of SP 9.5 asphalt, a 1" layer of SP 9.5, 4" ditch paving, construct a weir, finish grade the shoulders prior to placing sod, Maintenance of Traffic (MOT), stormwater pollution prevention, cleaning and grading ditches and/or shoulders to provide positive drainage, and sod beside the road and beside the ditch paving and in the ditch bottom where disturbed (all sod will be pinned).  The 1" layer of asphalt will not be placed until at least 30 days after the first lift is placed.

A Non-Mandatory Pre-Bid Meeting will be held on August 24, 2017 at 9:00 AM central time at the Jackson County Road Department.  Potential bidders are encouraged to attend.

The deadline for receipt of questions will be August 28, 2017 at 2:00 PM Central Time.  Questions must be submitted in writing to the County Engineer (email lalvarez@jacksoncountyfl.com: fax (850) 482-9063) with a copy to the Jeannie Bean (email jbean@jacksoncountyfl.com).

Bids will be opened and recorded at 1:10 PM (or immediately thereafter) on August 31, 2017 at the Jackson County Board of County Commissioners Board Room at 2864 Madison Street.  Bids may also be submitted to the County Engineer at the Board Room from 12:50 PM until 1:10 PM Central Time.

Bid documents will be open for public inspection after noon on August 14, 2017 at the Road and Bridge office at 2828 Owens Street.  Bid documents can be obtained from:

County Engineer

Attn:  Larry Alvarez

2828 Owens Street

Marianna, Florida  32446

(850) 482-9677

upon payment of $   No Charge           per set which amount constitutes the cost of reproduction and handling.

The Owner reserves the right to waive any informality or to reject any or all bids.  Each Bidder must deposit with his/her bid, security in the amount, form and subject to the conditions provided in the Information for Bidders.  Sureties used for obtaining bonds must appear as acceptable according to the Department of Treasury Circular 570.  Bidders must be Pre-approved by FDOT or Jackson County and in good standing with FDOT and the County.

No bid may be withdrawn for a period of sixty days after the scheduled closing time for receipt of bids.

To the extent applicable to this project, attention of Bidders is particularly called to the requirements of the Special Provisions, conditions of employment to be observed, and minimum wage rates to be paid under the Contract (if applicable), Section 3, Segregated Facilities, Section 109 Executive Order 11246, and all applicable laws and regulations of the Federal government and State of Florida, and bonding and insurance requirements.

MINORITIES AND FEMALE CONTRACTORS AND SUBCONTRACTORS ARE ENCOURAGED TO BID.

IN PARTICULAR, BIDDERS SHOULD NOTE THE REQUIRED ATTACHMENTS AND CERTIFICATIONS TO BE EXECUTED AND SUBMITTED WITH THE FORM OF BID PROPOSAL.

DATE:	___________________	_________________________

EQUAL OPPORTUNITY EMPLOYER

HANDICAP ACCESSIBLE/FAIR HOUSING JURISDICTION