SECTION 00010

ADVERTISEMENT FOR BIDS

PROJECT NAME:     Merritts Mill Road from US 90 to SR 71

Sealed bids, submitted in triplicate, will be received by the Board of County Commissioners of Jackson County, Florida, (Owner), until     1:00 p.m. (Central Time)  August 9, 2018    at the County Engineer’s Office (County Engineer, Larry Alvarez), 2828 Owens Street, Marianna, FL 32446 for the construction of the following described Project:

Merritts Mill Road from US 90 to SR 71

The project is to resurface and pave Merritts Mill Road from US 90 to State Road 71 (approximately 1.5 miles).  The existing road is paved from US 90 to Dean Road (0.573 miles) and from Panhandle Road to SR 71 (0.17 miles).   These sections will be widened and resurfaced with tack coat and 1.5" of asphalt.  From Dean Road to Panhandle Road is dirt (0.7 miles).  This section will be paved with 8" of limerock, Prime Coat, 1.5" of Asphalt, plus a 1" surface layer of SP 9.5 asphalt.  The shoulders will be shaped and receive sod, all other exposed areas will receive seed and mulch, driveway aprons will be paved, cross drain pipes will be replaced as indicated including mitered ends or headwalls, all pipes will be cleaned prior to final inspection, ditches will be cleaned or graded to provide positive flow and at cross pipes, driveway pipes will be cleared of debris or replaced if indicated (including mitered ends), trees and brush will be trimmed as indicated to provide sufficient sight distance, pavement markings will be placed on the finish asphalt, and signs will be replaced as indicated.

A Non-Mandatory Pre-Bid Meeting will be held on July 19, 2018 at 9:00 AM Central Time at the Jackson County Road Department.  Potential bidders are encouraged to attend.

The deadline for receipt of questions will be August 2, 2018    at 2:00 PM Central Time.  Questions must be submitted in writing to the County Engineer (email lalvarez@jacksoncountyfl.com: fax (850) 482-9063) with a copy to the Jeannie Bean (email jbean@jacksoncountyfl.com).

Bids will be opened and recorded at 1:10 PM (or immediately thereafter) on  August 9, 2018  at the Jackson County Board of County Commissioners Board Room at 2864 Madison Street.  Bids may also be submitted to the County Engineer at the Board Room from 12:50 PM until 1:10 PM Central Time.

Plans, specifications, and contract documents will be open for public inspection after noon on   July 5, 2018   at the Road and Bridge office at 2828 Owens Street.  Bid documents must be obtained from:

Larry Alvarez, County Engineer

2828 Owens Street

Marianna, Florida  32446

(850) 482-9677

upon payment of $   No Charge           per set which amount constitutes the cost of reproduction and handling.  This payment will not be refunded.

The Owner reserves the right to waive any informality or to reject any or all bids.  Each Bidder must deposit with his/her bid, security in the amount, form and subject to the conditions provided in the Information for Bidders.  Sureties used for obtaining bonds must appear as acceptable according to the Department of Treasury Circular 570.  Bidders must be Pre-approved by FDOT or Jackson County and in good standing with FDOT and the County.

No bid may be withdrawn for a period of sixty days after the scheduled closing time for receipt of bids.

To the extent applicable to this project, attention of Bidders is particularly called to the requirements of the Special Provisions, conditions of employment to be observed, and minimum wage rates to be paid under the Contract (if applicable), Section 3, Segregated Facilities, Section 109 Executive Order 11246, and all applicable laws and regulations of the Federal government and State of Florida, and bonding and insurance requirements.

Minorities and female contractors and subcontractors are encouraged to bid.

IN PARTICULAR, BIDDERS SHOULD NOTE THE REQUIRED ATTACHMENTS AND CERTIFICATIONS TO BE EXECUTED AND SUBMITTED WITH THE FORM OF BID PROPOSAL.

EQUAL OPPORTUNITY EMPLOYER

HANDICAP ACCESSIBLE/FAIR HOUSING JURISDICTION