November 20, 2018

Request for Proposal: 	RFP1118WREREPLACEMENT - Weight Room Equipment Replacement and Installation

Addendum # 1

Question

Question 1:	What are the specifications of the elliptical machines and recumbent bicycles?

Response:	Provide proposals for full, commercial grade ellipticals and recumbent bicycles.

The quoted ellipticals should have the following specifications or similar:

- Welded Steel Frame

- Console

- Moving handlebars

- Ramp adjustment range from 10 to 35 degrees

- Stride Length: 18” to 21”

- Resistance Levels: 20 to 25

- Heart rate monitor

- Covered drive housing

- Approximate dimensions (L x W x H): 82-86” x 28-30” x 66-68”

- Approximate weight: 250-300 lbs

- Equipment Power: Self-powered or self-generating

- Console Power: 120V

- Frame Warranty: Lifetime

- Parts Warranty: Minimum of 5 years

The quoted recumbent bicycles should have the following specifications or similar:

- Welded Steel Frame

- Console

- Side handlebars

- Step-through design

- Comfortable, ergonomic recumbent seat back

- Adjustable seat

- Resistance Levels: 20-30

- Heart rate monitor

- Approximate dimensions (L x W x H): 63-66” x 23-30” x 45-49”

- Approximate weight: 160-200 lbs

- Equipment Power: Self-powered or self-generating

- Console Power: 120V

- Frame Warranty: Lifetime

- Parts Warranty: Minimum of 5 years

End of Addendum #1